## Slide 1: Knowledge is Power
Part 1.0 Accurately Measuring Watt Hours/Mile
Ted Lowe 1/16/2009 http://tedlowe.fveaa.org

## Slide 2: Table of Contents
  What is Watt Hours/Mile ?
  Why should we measure it ?
  How do we measure it ?
  What to do with measurements ?

## Slide 3: What is Watt Hours/Mile ?
  It's a measure of how much power is used to do a certain amount of work.
  EG, MPG = Miles per Gallon
  WH/M or MPG varies based on vehicle, driving techniques, accessory usage, terrain, speed, temperature, etc.
  We pay our electric bill based on how much power we have used.
  We pay based on how many KWH (Kilo-Watt-Hours) we used.

## Slide 4: What is Watt Hours/Mile ? (2)
  KWH = 1000 Watt/Hour = 10 x 100 Watt light bulbs on for 1 hour.
  Current ComED KWHs cost about 15 cents.
  EG, My S10 EV takes about 20 KWH to charge and i can drive about 50 miles on a charge, so my APPROXIMATE CALCULATED AVERAGE WH/M is 20,000 / 50 = 400
  Bicycling is approx 25-50, Walking is approx. 128 and Prius is about 250.

## Slide 5: Why Measure WH/M?
  Notice prior use of words like "about", "average", "approximately", "calculated", etc.
  Measuring gives us real world FACTS. It helps us to further quantify our understanding.
  We can use FACTS in our own lives and in our EV outreach mission.

## Slide 6: Why Measure WH/M? (2)
We can confidently answer questions like:
  What is my remaining range?
  What is the most efficient speed to drive ?
  Is it more efficient to drive 45 MPH in 3rd, 4th or 5th gear ?
  How much does AC use affect my range?
  How does the cold temperatures affect my range ?

## Slide 7: Why Measure WH/M? (3)
More answerable questions:
  What was the effect of my last vehicle upgrade?
  How do my driving habits effect my range ?
  Is there something wrong with my EV ?
  Did i leave the emergency brake on ?
  Why other answers do you want ???
KNOWLEDGE ABOUT POWER !

## Slide 8: Accurately Measuring WH/M
Finally the good stuff :-)
To measure WH/M we need to measure:
  Power (watts)
  Time (hours)
  Distance (miles)
And then "do the math" :-)

## Slide 9: Electric Power Relationships
Measuring Power - Dog-Ear this page!
Ohm's Law: V = I * R
Voltage (volts) = Current (amps) * Resistance (ohms)
Joule's Law: P = V * I
Power (watts) = Voltage (volts) * Current (amps)

## Slide 10: Ohm's Law
V = I * R
EG: V = 1 volt battery, R = 1 ohm resistor
How much current (I) will flow ?

## Slide 11: Joule's Law
P = V * I
or by substituting
Ohm's law V=I*R
P = I^2 * R
Note: Power is proportional to square of Current!
EG: V = 1 volt battery, R = 1 ohm resistor
How much power will R consume ? 1 watt

## Slide 12: Measuring Power
P = V * I
We need to measure two of the three variables:
V, I and/or R
We'll measure V and I as follows

## Slide 13: Measuring Voltage
The really old way
Newer Way

## Slide 14: Measuring Voltage (2)
Newest Way = Analog to Digital Converter (ADC)
Converts an analog voltage to a digital value so a computer (microcontroller) can process it.

## Slide 15: Measuring EV's Voltage
  Our EV pack voltages are quite high, eg, 160VDC.
  ADC chips don't handle voltages that high
  Must "divide to conquer"!
  Voltage Divider:

## Slide 16: Measuring EV's Voltage (2)
EG, My S10 Pack (120 V):
Vin = 160 V (final charge)
R1 = 200K ohms R2 = 6.5K ohms
Most of Vin will be across the "most resistive" resistor R1, with only 1/32 of it across R2 (1/32 = 6.5/200)
Vout = 5 V (within ADC range)

## Slide 17: Measuring EV's Voltage (3)
The ADC will measure 5V = 4+1 = 00000000101
convert back to whole measurement by multipying by 32 (shift 5 positions right)
00010100000 = 128+32 = 160 (bingo:-)
OK, we have the Voltage measurement in digital form, now lets move onto the Current...

## Slide 18: Measuring Current Via Shunt
  A shunt is just a very accurate ultra-low value high-wattage resistor.
  Most of our EVs have shunts connected to ammeters to show our current draw.
  EG, a shunt that will handle 500A (max)
Deltec MKB-500-50

## Slide 19: Deltec MKB-500-50 Shunt
The 500-50 in the part number means:
500 A (max) flowing through it will generate a
50 mV voltage across it.
IE, .1mV for each amp flowing (1 milliVolt = .001 V)
Exercises for motivated students: How much power will be dissipated by the shunt with 100A (nominal cruising speed) flow ? 500A (hard acceleration) ? You may be surprised!

## Slide 20: Measuring Current With ADC
  EG, cruising along drawing 100A
  Shunt would have 10mV across it
  Very small number (opposite of high voltage problem before)
  Need to amplify before measuring with the ADC
  Will use a precision instrumentation amplifer IC like the TI OPA344 (using findchips.com, Digi-Key sells for $1.30 quantity 1)
  Will amplify by 100 to give 5V for 500A (within the ADC range)

## Slide 21: Calculating Power
Joule's Law: P = V * I
EG, My S10 with a freshly charged battery pack (125V) cruising at 100A draw = 12,500 watts
The battery pack voltage (V) and amperage draw (I) will fluctulate while driving, so they must be frequently measured (sampled) and stored to be able to accurately calculate Watt-Hours/Mile.
Please come back for Part 1.1 !